## Slide 1: MULTI SENSOR HAPTIC HEADSET
ASME Assistive Tech
Project Showcase

## Slide 2: Problem & Solution
Challenge: Visually impaired users lack real-time obstacle awareness.
Our Solution: Wearable headset with ultrasonic sensors + vibration motors.

## Slide 3: Hardware Overview
Arduino Nano
5 × HC-SR04 ultrasonic sensors (front and sides)
5 × vibration motors
(mapped 1:1 to sensors)
Powered by 9V battery.

## Slide 4: Software & Modes
Normal Mode: continuous vibration strength ∝ distance
Change Mode: pulses when object moves > 10 cm
Radar Mode: pulsing rate speeds up as you get closer
Mode Switch: hold hand < 5 cm for 2 s → cycles modes

## Slide 5: Key Features & Benefits
Intuitive haptic feedback for direction + proximity
Burst alerts when obstacles span two sensors (size cue)
Easy mode switching, clear debug logs in Serial Monitor
Smooth intensity transitions with PWM ramping

## Slide 6: How it works
Power on headset & open Serial Monitor
Walk toward obstacle → motors vibrate stronger
Move object between two sensors → burst alert
Hold hand at sensor → mode change beeps + new pattern

## Slide 7: Next Steps & Future Work
Add Bluetooth for remote monitoring & on-the-fly calibration
Add a hardware button to cycle modes so it survives power-cycles.